## Slide 1: Museum Alarm System Final Presentation – Group 4
Léo Dumas - leo.dumas@tum.de
Lukas Obkircher - lukas.obkircher@tum.de
Filippo Fuochi – filippo.fuochi@tum.de
Advisors: Vilgelm Mikhail: mikhail.vilgelm@tum.de
Samuele Zoppi: samuele.zoppi@tum.de

## Slide 2: Idea
Wireless alarm network for a museum
  Protect from thefts during closed hours (Movement detection)
  Protect from vandalism during open hours (Close detection)
  Avoid system failures
A
  Give background on the topic
  What are the common problems?
  What are the state-of-the-art solutions and approaches?

## Slide 3: Overview
Network principle
Material
  Motes
  Sensors
Routing protocol
System behavior
Addition features

## Slide 4: Network Overview
One central mote connected to a computer
  Manage the network state
    If an alarm is launched
    If all the motes are alive
  Manage the entire routing protocol
  Recovery procedures
  Configuration of each mote
  Visual Interface for a complete visualization in real time
6 motes with embedded sensors
  Connected to the power supply
  Manage
    Close detection : if someone tries to touch/steal a painting
    Movement detection
  Form an interconnected multi-hop network
  Don’t store any routing table/knowledge of the network

## Slide 5: Material

## Slide 6: Network Principle
2 types of routing protocols for transmissions : controlled flooding and unicast
Controlled flooding : 3 different modes/packages
  We use an On-Demand-Protocol to build the routing table : Dynamic Source Routing => route request (RREQ) or FSearch Mode / route reply (RREP) or FAck Mode
  If a mote launch an alarm, it floods the network to reach quickly the central mote => FAlarm Mode

## Slide 7: Network Principle
Unicast : 3 different modes/packages
  When the routing table is built, we send a message to each mote according to the stored path to check if it is alive => Search Mode
  The mote then responds => Alive Mode If we don’t receive this message in a certain time (path less reliable or other problems) we again use the Dynamic Source Routing for this mote and display the indication on the Visual Interface.
  For opening hours we don’t use Sonar sensors so we have to desactivate the ability to detect and launch an alarm => Config Mode

## Slide 8: Focus on the packages – Unicast
=> Alive Package
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 0 = Search | Hopcount | Path |  | 
=> Search Package
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 1 = Alive | Hopcount | Path |  | 
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Status | Dest-ID | 2 = Config | Hopcount | Path |  | 
=> Config Package
0 = nothing
1 = NO_SENSOR

## Slide 9: Focus on the packages – Controlled Flooding
=> FSearch Package
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 3 = FAlarm | MSG-ID | Sensor Type | Distance-H | Distance-L
=> FAlarm Package
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 4 = FSearch | MSG-ID |  |  | 
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 5 = FAck | SUM-RSSI | Path |  | 
=> FAck Package
0 = IR
1 = SONAR
2 = NO_SENSOR
MSB (cm)
LSB (cm)

## Slide 10: Routing Protocol - Principle
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
Principle
Flooding search for each motes to find the best path
Messages for different targeted mote have a different message ID (incrementation)
The targeted mote responds to the first message it receives by a flooding to central station
Central station build the routing table, taking the best path for each mote according to our standards : reliability and fastness

## Slide 11: Routing Protocol – FSearch Mode
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Flooding to Mote 1 – Step1
Controlled flooding => check if message ID is newer than the previous one
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 4 = FSearch | MSG-ID |  |  | 
Content | 0 | 1 | 4 | 1 |  |  | 

## Slide 12: Routing Protocol – FSearch Mode
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Flooding to Mote 1 – Step2
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 4 = FSearch | MSG-ID |  |  | 
Content | 0 | 1 | 4 | 1 |  |  | 
Controlled flooding => Message received, FSearch for mote 1 finished

## Slide 13: Routing Protocol – FAck Mode
Central Station
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Flooding to central mote : general view
SUM-RSSI : After each message ride, we add in its packet the RSSIs greater than a threshold (70)

## Slide 14: Routing Protocol – FAck Mode
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Ack from Mote 1 – Exemple for one path – Step1
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 5 = FAck | SUM-RSSI | Path |  | 
Content | 1 | 0 | 5 | 0 |  |  | 

## Slide 15: Routing Protocol – FAck Mode
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Ack from Mote 1 – Exemple for one path – Step2
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 5 = FAck | SUM-RSSI | Path |  | 
Content | 1 | 0 | 5 | 0 | 2 |  | 
RSSI=60<70

## Slide 16: Routing Protocol – FAck Mode
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Ack from Mote 1 – Exemple for one path – Step3
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 5 = FAck | SUM-RSSI | Path |  | 
Content | 1 | 0 | 5 | 0+5 | 2 | 3 | 
Controlled flooding => Message received, FSearch for mote 1 finished
RSSI=75>70

## Slide 17: Routing Protocol – FAck Mode
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Ack from Mote 1 – Exemple for one path – Step4
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 5 = FAck | SUM-RSSI | Path |  | 
Content | 1 | 0 | 5 | 5+2 | 2 | 3 | 
Controlled flooding => Message received, FSearch for mote 1 finished
RSSI=72>70

## Slide 18: Routing Protocol – Routing table construction
=> Received Message 1 from Mote1
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 5 = FAck | SUM-RSSI | Path |  | 
Content | 1 | 0 | 5 | 5+2 | 2 | 3 | 
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Mote-ID | Found | SUM-RSSI | Hops | Path |  | 
Content | 1 | 1 | 7 | 2 | 2 | 3 | 
=> Routing Table
First Ack answer from 1 => path stored

## Slide 19: Routing Protocol – Routing table construction
=> Received Message 2 from Mote2
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 5 = FAck | SUM-RSSI | Path |  | 
Content | 1 | 0 | 5 | 0 | 4 | 5 | 6
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Mote-ID | Found | SUM-RSSI | Hops | Path |  | 
Content | 1 | 1 | 0 | 3 | 4 | 5 | 6
=> Routing Table
SUM-RSSI smaller => path stored

## Slide 20: Routing Protocol – Routing table construction
=> Received Message 3 from Mote1
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 5 = FAck | SUM-RSSI | Path |  | 
Content | 1 | 0 | 5 | 0 | 2 |  | 
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Mote-ID | Found | SUM-RSSI | Hops | Path |  | 
Content | 1 | 1 | 0 | 1 | 2 |  | 
=> Routing Table
SUM-RSSI is equal but the number of hops is smaller => path stored

## Slide 21: Routing Protocol – Routing table construction
=> Received Message 4 from Mote1
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 5 = FAck | SUM-RSSI | Path |  | 
Content | 1 | 0 | 5 | 10 |  |  | 
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Mote-ID | Found | SUM-RSSI | Hops | Path |  | 
Content | 1 | 1 | 0 | 1 | 2 |  | 
=> Routing Table
SUM-RSSI is worst even if direct connection=> path not stored

## Slide 22: System Behavior (closing hours) – Step 1
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Search mode – Mote1
Routing table has been built.
We search with unicast Mote 1 : the stored path is 2.
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 0 = Search | Hopcounts | Path |  | 
Content | 0 | 1 | 0 | 1 | 2 |  | 

## Slide 23: System Behavior – Step 2
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Search mode – Mote1
When a mote forwards a message, the hopcount is decreased.
=> Hopcount = 0 signifies direct connection
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 0 = Search | Hopcount | Path |  | 
Content | 0 | 1 | 0 | 0 | 2 |  | 

## Slide 24: System Behavior – Step 3
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Alive mode – Mote1
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 1 = Alive | Hopcount | Path |  | 
Content | 1 | 0 | 1 | 1 | 2 |  | 

## Slide 25: System Behavior – Step 4
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Alive mode – Mote1
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 1 = Alive | Hopcount | Path |  | 
Content | 1 | 0 | 1 | 0 | 2 |  | 

## Slide 26: System Behavior – Step 5
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Search mode – Mote2
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 0 = Search | Hopcount | Path |  | 
Content | 0 | 2 | 0 | 0 |  |  | 

## Slide 27: System Behavior – Step 6
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Alive mode – Mote2
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 1 = Alive | Hopcount | Path |  | 
Content | 2 | 0 | 1 | 0 |  |  | 

## Slide 28: System Behavior – Step 7
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Search mode – Mote3
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 0 = Search | Hopcount | Path |  | 
Content | 0 | 3 | 0 | 0 |  |  | 

## Slide 29: System Behavior – Step 8
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Alive mode – Mote3
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 1 = Alive | Hopcount | Path |  | 
Content | 3 | 0 | 1 | 0 |  |  | 

## Slide 30: System Behavior – Step 9
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Search mode – Mote4
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 0 = Search | Hopcount | Path |  | 
Content | 0 | 4 | 0 | 2 | 5 | 3 | 

## Slide 31: System Behavior – Step 10
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Search mode – Mote4
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 0 = Search | Hopcount | Path |  | 
Content | 0 | 4 | 0 | 1 | 5 | 3 | 

## Slide 32: System Behavior – Step 11
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Search mode – Mote4
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 0 = Search | Hopcount | Path |  | 
Content | 0 | 4 | 0 | 0 | 5 | 3 | 

## Slide 33: System Behavior – Step 12
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Alive mode – Mote4
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 1 = Alive | Hopcount | Path |  | 
Content | 4 | 0 | 1 | 2 | 5 | 3 | 

## Slide 34: System Behavior – Step 13
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Alive mode – Mote4
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 1 = Alive | Hopcount | Path |  | 
Content | 4 | 0 | 1 | 1 | 5 | 3 | 

## Slide 35: System Behavior – Step 14
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Alive mode – Mote4
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 1 = Alive | Hopcount | Path |  | 
Content | 4 | 0 | 1 | 0 | 5 | 3 | 

## Slide 36: System Behavior – Step 15
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Search mode – Mote5
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 0 = Search | Hopcount | Path |  | 
Content | 0 | 5 | 0 | 1 | 6 |  | 

## Slide 37: System Behavior – Step 16
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Search mode – Mote5
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 0 = Search | Hopcount | Path |  | 
Content | 0 | 5 | 0 | 0 | 6 |  | 

## Slide 38: System Behavior – Step 17
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Alive mode – Mote5
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 1 = Alive | Hopcount | Path |  | 
Content | 5 | 0 | 1 | 1 | 6 |  | 
A problem occurs !
Maybe it’s due to the mote, congestion, cross-traffic or it was to slow (the timer for the unicast is 2 seconds).

## Slide 39: System Behavior – Step 18
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> FSearch mode – Mote5
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 4 = FSearch | MSG-ID |  |  | 
Content | 0 | 5 | 4 | 1 |  |  | 
After 2 seconds, Alive not received
=> Recovery Procedure :
again Dynamic Source Routing for Mote5 and display a warning.
!! Warning Mote5 !!

## Slide 40: System Behavior – Step 19
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> FSearch mode – Mote5
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 4 = FSearch | MSG-ID |  |  | 
Content | 0 | 5 | 4 | 1 |  |  | 
!! Warning Mote5 !!

## Slide 41: System Behavior – Step 20
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> FAck mode – Mote5
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 5 = FAck | SUM-RSSI | Path |  | 
Content | 5 | 0 | 5 | 0 |  |  | 
!! Warning Mote5 !!

## Slide 42: System Behavior – Step 21
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> FAck mode – Mote5
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 5 = FAck | SUM-RSSI | Path |  | 
Content | 5 | 0 | 5 | 1 | 6 |  | 
!! Warning Mote5 !!
Central Station receives several messages and store the best path.
Because we receive something from Mote5, the warning can be removed by the user if he wants (or maybe he will do a security check).

## Slide 43: System Behavior – Step 22
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Search mode – Mote6
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 0 = Search | Hopcount | Path |  | 
Content | 0 | 6 | 0 | 0 |  |  | 
We continue our security unicast check where we stopped it.

## Slide 44: System Behavior – Step 23
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Alive mode – Mote6
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 1 = Alive | Hopcount | Path |  | 
Content | 6 | 0 | 1 | 0 |  |  | 

## Slide 45: System Behavior – Step 24
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Search mode – Mote1
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 0 = Search | Hopcount | Path |  | 
Content | 0 | 1 | 0 | 1 | 2 |  | 
We start over the unicast alive check.
The paths have not changed if there wasn’t any issue.

## Slide 46: System Behavior – Step 25
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
=> Search mode – Mote1
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 3 = FAlarm | MSG-ID | Sensor Type | Distance-H | Distance-L
Content | 5 | 0 | 3 | 1 | 0 | 2 | 28
Alarm launched by Mote5 using controlled flooding.
Mote5 has a Sonar sensor (movement detected at 5.4m).
=> Falarm mode – Mote5

## Slide 47: System Behavior – Step 26
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Source-ID | Dest-ID | 3 = FAlarm | MSG-ID | Sensor Type | Distance-H | Distance-L
Content | 5 | 0 | 3 | 1 | 0 | 2 | 28
=> Falarm mode – Mote5
!! Alarm Mote5 !!

## Slide 48: System Behavior – Step 27
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Status | Dest-ID | 2 = Config | Hopcount | Path |  | 
Content | 1 | 5 | 2 | 1 | 6 |  | 
=> Config mode – Mote5
After a while, it’s the opening hours and we want to change to NO-SENSOR the SONAR motes.
For example mote5.

## Slide 49: System Behavior – Step 28
Central Station
0
Mote 6
Mote 5
Mote 2
Mote 4
Mote 3
Mote 1
Byte | 0 | 1 | 2 | 3 | 4 | 5 | 6
Description | Status | Dest-ID | 2 = Config | Hopcount | Path |  | 
Content | 1 | 5 | 2 | 0 | 6 |  | 
=> Config mode – Mote5
Mote5 sonar is desactivated.

## Slide 50: Prior Work and Open Issues
This work is based on:
  Previous Master/Diploma/Bachelor Thesis
  Papers …
  Advisor’s proposal …
What has been done before – what is available:
  Earlier results
  Available models
  Available tools
  …
What is new or additionally required:
  Developed, improved models
  Developed, improved software/tools
  Novel results
for the Kick Off Presentation use these points to narrow down the goal of the thesis

## Slide 51: Summary of Thesis Results
Summarize your contribution
  Explain chosen approach
  Show results, e.g. simulations
  What are the strengths/weaknesses?
  What are the implications?
Give outlook/make suggestions for further work
  What could not be done due to time limitations?
  Any unsolved problems that occurred?
  Any extensions which would be nice to have?
Instead of your contribution and an outlook, in the Kick Off Presentation you can say here, what general findings you are expecting, e.g., the new method A is expected to handle more users than the previous method B, but might have more overhead. In the results these findings will be quantified.

## Slide 52: Figures Showing Results
Labels for axis and annotations have to be readable!
Fonts should be the same as in the presentation
Consider only colors that are not too bright (Here green is maybe not the best choice)
Always add one sentence concluding your observations

## Slide 53: References
[1] Keshav, S. (2007). How to read a paper. ACM SIGCOMM Computer Communication Review, 37(3), 83.
[2] Levin et al. (2012). Logically centralized?: state distribution trade-offs in software defined networks. In Proceedings of the first workshop on Hot topics in software defined networks - HotSDN ’12 (p. 1). Workshop/conference venue

## Slide 54
Questions?

## Slide 55: Notes/Hinweise
This template shows only the most important slides to be considered for your presentation
You may add any additional slides to explain the approach, methods, simulation setup, results, evaluation … details
Some indications are given in callouts in the template already
For the Final Presentation it is recommended to have an executive summary at the beginning, e.g. after the motivation, and a summary with an outlook at the end (for both slide 5 could serve as a template).
Always add references!